## Slide 1
ForgeLine | Product Alpha | 2026-08-11
Measurement work instruction training
A short operator reference for controlled Product Alpha dimensional checks
Objective
Measure consistently, record clearly, and contain any condition outside the approved band.
Critical acceptance band
Nominal requirement
±0.18 mm
Synthetic training material | No production identifiers or personal data

## Slide 2
ForgeLine | Product Alpha | 2026-08-11
Stable measurement system
A clean, zeroed gage makes the result defensible
1. Prepare the surface
Remove residue from the caliper jaws and the Product Alpha measurement surface.
2. Confirm zero
Close the jaws gently, set zero, then repeat once to verify stability.
3. Measure at IP-03
Contact the specified critical-width surfaces without force or burr interference.

## Slide 3
ForgeLine | Product Alpha | 2026-08-11
Record the result while the sample is present
An inspection record must connect the method, value, and disposition
Required record fields
Sample alias, IP-03, nominal requirement, actual millimetre value, gage status, and PASS or HOLD.
Pass condition
Measured value remains inside the nominal ±0.18 mm acceptance band.
Escalation condition
If the result is out of band or gage confidence is uncertain, stop and begin NCR-026 containment.

## Slide 4
ForgeLine | Product Alpha | 2026-08-11
Containment workflow
Contain first, document second, release only with quality disposition
Contain
Label the sample HOLD and prevent forward movement under NCR-026.
Document
Capture the observed value, inspection point, sample alias, and gage status.
Screen and disposition
Screen comparable samples with the same method; quality records the release or next action.